## Slide 1: Digital Design
With an Introduction to the Verilog HDL, VHDL, and SystemVerilog
6th Edition, Global Edition
Chapter 01
Digital Systems and Binary Numbers

## Slide 2
CPU

## Slide 3
Analog/Digital
B = Byte
b = bit
1 B = 8 b

## Slide 4: Powers of Two
Why is 2n?
210= 1Kilo
220 = 1Mega
230 = 1Giga
240 = 1Tera

## Slide 5: Numbers with Different Base

## Slide 6
Number Base Conversion
a5a4a3a2a1a0.a-1a-2a-3
= anrn+an-1rn-1+...+a2r2+a1r+a0+a-1r-1+a-2r-2+...+a-mr-m
7392 = 7 × 103 + 3 × 102 + 9 × 101 +2 × 100
(11010.11)2 =1×24+1×23+0×22+1×21+0×20+1×2-1+1×2-2
= (26.75)10

## Slide 7
Number Base Conversion
Convert decimal 41 to binary.
answer : (41)10 = (a5a4a3a2a1a0)2 = (101001)2
answer : (41)10 = (a5a4a3a2a1a0)2 = (101001)2
 | Integer Quotient |  | Remainder | Coefficient
41/2 = | 20 | + | ½ | a0 = 1
20/2 = | 10 | + | 0 | a1 = 0
10/2 = | 5 | + | 0 | a2 = 0
5/2 = | 2 | + | ½ | a3 = 1
2/2 = | 1 | + | 0 | a4 = 0
1/2 = | 0 | + | ½ | a5 = 1
Integer | Remainder
41 | 
20 | 1
10 | 0
5 | 0
2 | 1
1 | 0
0 | 1
Answer
=101001

## Slide 8
Number Base Conversion
Convert decimal 153 to octal.
Convert (0.6875)10 to binary.
153 | 
19 | 1
2 | 3
0 | 2 = (231)8
 | Integer |  | Fraction | Coefficient
0.6875*2 = | 1 | + | 0.3750 | a-1 = 1
0.3750*2 = | 0 | + | 0.7500 | a-2 = 0
0.7500*2 = | 1 | + | 0.5000 | a-3 = 1
0.5000*2 = | 1 | + | 0.0000 | a-4 = 1
Answer:(0.6875)10 = (0.a-1a-2a-3a-4)2 = (0.1011)2

## Slide 9
Octa – Hex Number Conversion
( 10 110 001 101 011 . 111 100 000 110 )2 = (26153.7460)8
2 6 1 5 3 7 4 0 6
( 10 1100 0110 1011 . 1111 0010 )2 = (2C6B.F2)16
2 C 6 B F 2

## Slide 10
Complements
(r-1)’s complements of N is (rn-1)-N
r=10, r-1=9, 9’complements of N is (10n-1)-N
Ex) the 9’s complements of 546700 is 999999-546700 = 453299
the 9’s complements of 012398 is 999999-012398 = 987601
For binary number, r=2, r-1=1
1’complements of N is (2n-1)-N
Ex) the 1’s complements of 1011000 is 0100111
the 1’s complements of 0101101 is 1010010

## Slide 11: Signed Binary Numbers

## Slide 12
Subtraction with Complements
X=1010100, Y=1000011, (a) X-Y, (b) Y-X
(a) X-Y
(b) Y-X
X = | 1010100
2’s complement of Y = | +0111101
Sum = | 10010001
Discard end carry 27 = | -10000000
Answer: X-Y = | 0010001
Y = | 1000011
2’s complement of X = | +0101100
Sum = | 1101111
There is no carry.
The answer is Y-X = -(2’s complement of 1101111)=-0010001

## Slide 13
Signed Binary Numbers
Arithmetic Addition
  signed-magnitude system follows the rules of ordinary arithmetic
  signed-complement system requires only addition.
+6 |  | 00000110 |  | -6 |  | 11111010
+13 |  | 00001101 |  | +13 |  | 00001101
+19 |  | 00010011 |  | +7 |  | 00000111
+6 |  | 00000110 |  | -6 |  | 11111010
-13 |  | 11110011 |  | -13 |  | 11110011
-7 |  | 11111001 |  | -19 |  | 11101101

## Slide 14: Binary-Coded Decimal (BCD).

## Slide 15
Binary Code – BCD Code
the 4-bit code for one decimal
  (185)10 = (0001 1000 0101)BCD = (10111001)2
BCD Addition
If the binary sum is greater or equal to 1010, we add 0110 to obtain the correct BCD
4 |  | 0100 |  | 4 |  | 0100 |  | 8 |  | 1000
+5 |  | +0101 |  | +8 |  | +1000 |  | +9 |  | +1001
9 |  | 1001 |  | 12 |  | 1100 |  | 17 |  | 10001
 |  |  |  |  |  | +0110 |  |  |  | +0110
 |  |  |  |  |  | 10010 |  |  |  | 10111

## Slide 16: Four Different Binary Codes for the Decimal Digits.

## Slide 17: Gray Code

## Slide 18: American Standard Code for Information Interchange (ASCII).

## Slide 19: Transfer of information among registers.

## Slide 20: Truth Tables of Logical Operations

## Slide 21: Symbols for digital logic circuits.

## Slide 22: Gates with multiple inputs.

## Slide 23: Signal levels for binary logic values.

## Slide 24: Input–output signals for gates.