## Slide 1: Digital Design
With an Introduction to the Verilog HDL, VHDL, and SystemVerilog
6th Edition, Global Edition
Chapter 02
Boolean Algebra and Logic Gates

## Slide 2: Postulates and Theorems of Boolean Algebra

## Slide 3: Truth Tables for F1 and F2
F1 = x + y’z
F2 = x'y'z + x'yz +xy‘
= x'z(y'+y) + xy'
= x'z + xy'

## Slide 4: Logic (Gate) Diagram for the Boolean Function F1 = x + y'z

## Slide 5: Implementation of Boolean Function F2 with Gates

## Slide 6: Truth Tables for F1 and F2
Simplify the following Boolean functions to a minimum number of literals
  x(x'+y) = xx' + xy = 0 + xy = xy
  x +x'y = (x+x')(x+y) = 1(x+y) = x + y
  (x+y)(x+y') = x + xy + xy' + yy' = x(1+y+y') = x
  xy + x'z + yz = xy + x'z + yz(x+x') = xy + x'z + xyz + x'yz
= xy(1+z) + x'z(1+y) = xy + x’z
5. (x+y)(x'+z)(y+z) = (x+y)(x'+z) : by duality from function 4.
(A + B + C)'= (A+x)' let B+C=x
= A'x' by theorem 5(a)(DeMorgan)
= A'(B+C)' substitute B+C=x
= A'(B'C') by theorem 5(a)(DeMorgan)
= A'B'C' by theorem 4(b)(associative)
=> (A+B+C+D+…+F)' = A'B'C'D'…F'
(ABCD…F)' = A' +B'+ C' + D' + … + F'

## Slide 7: Complement of a Function
Find the complement of the functions
F1=x'yz'+x'y’z,
F2=x(y'z'+yz).
F1' = (x'yz'+x'y'z)' = (x'yz')'(x'y'z)' = (x+y'+z)(x+y+z')
F2' = [x(y'z'+yz)]' = x'+(y'z'+yz)' = x'+(y'z')'(yz)' = x'+(y+z)(y'+z')

## Slide 8: Minterms and Maxterms for Three Binary Variables

## Slide 9: Functions of Three Variables
f1 = x'y'z+xy'z'+xyz = m1+m4+m7
f2 = x'yz+xy'z+xyz'+xyz = m3+m5+m6+m7
f1 = (x+y+z)(x+y'+z)(x+y’+z’)(x'+y+z')(x'+y'+z)
= M0M2M3M5M6
f2 = (x+y+z)(x+y+z‘)(x+y'+z)(x'+y+z)
= M0M1M2M4

## Slide 10: Sum of Minterms (e.g. F = A + B’C)
Express the Boolean function F=A+B'C in a sum of minterms.
A = A(B+B') = AB +AB'
= AB(C+C') + AB'(C+C')
= ABC + ABC' + AB'C +AB'C'
B'C = B'C(A+A') = AB'C + A'B'C
F = A + B'C
= A' B'C + AB'C' + AB'C + ABC' + ABC
= m1 + m4 + m5 + m6 + m7
= ∑(1, 4, 5, 6, 7)

## Slide 11: Truth Table for F = xy + x'z

## Slide 12: Product of Maxterms (e.g. F = xy + x’z)
Express the Boolean function F = xy + x'z in a product of maxterm form.
F = xy + x'z = (xy+x')(xy+z)
= (x+x')(y+x')(x+z)(y+z)
= (x'+y)(x+z)(y+z)
x' + y= x' + y + zz'= (x'+y+z)(x'+y+z')
x + z= x + z + yy'= (x+y+z)(x+y'+z)
y + z= y + z + xx'= (x+y+z)(x'+y+z)
F = (x+y+z)(x+y'+z)(x'+y+z)(x'+y+z')
= M0M2M4M5
F(x, y, z) = ∏(0, 2, 4, 5)

## Slide 13: Conversion btw. Canonical Forms
Conversion between sum of minterms and product of maxterms
F(A, B, C) = ∑(1, 4, 5, 6, 7)
F' (A, B, C) = ∑(0, 2, 3) = m0 + m2 + m3
F = (m0+m2+m3)' = m0'm2'm3' = M0M2M3 = ∏(0, 2, 3) , mj' = Mj
Ex) F = xy + x'z
F(x, y, z) = ∑(1, 3, 6, 7)
F(x, y, z) = ∏(0, 2, 4, 5)

## Slide 14: Two-level Implementation (Standard Forms)

## Slide 15: Figure 2.4 Three- and Two-level Implementation

## Slide 16: Boolean Expressions for the 16 Functions of Two Variables

## Slide 17: Digital Logic Gates

## Slide 18: Multiple-input and Cascaded NOR and NAND Gates

## Slide 19: Three-input Exclusive-OR Gate

## Slide 20: Signal Assignment and Logic Polarity